The Standard
C++ Library
Version 1: Dr. Ofir Pele
Version 2: Dr. Erel Segal-Halevi

---
Main Ideas
Main Ideas
Purpose
Flexibility
Efficiency
Simple & Uniform Interface

---
Q: What types can we put
in a template param?
A: Type which models the
requested concept.

---
Concepts - Example
Concepts - Example
Consider:
The user must provide a type that has a less-than operator (<) to compare two values of type T, the result of which must be convertible to a Boolean value
template<typename T> const T& min(const T& x,
    const T& y)
{
   return x < y? x : y;
}

---
Concepts - Example
Concepts - Example
Consider:
The user must provide a type that has a less-than operator (<) to compare two values of type T, the result of which must be convertible to a Boolean value
template<typename T> const T& min(const T& x,
    const T& y)
{
   return x < y? x : y;
}
The problem:
cryptic error messages
from the implementation of the function
instead of a clear error message

---
Concepts – What we would like it to be:
Concepts – What we would like it to be:
Not C++ syntax:
The user must provide a type that has a less-than operator (<) to compare two values of type T, the result of which must be convertible to a Boolean value
template<LessThanComparable T> const T& min(const T& x,
        const T& y)
{
   return x < y? x : y;
}

---
Concepts
Concepts
Concepts are not a yet part of the C++ language,
Currently there is no (standard) way to declare a concept in a program, or to declare that a particular type is a model of a concept
“were not ready” for C++11,C++14,C++17
C++-20 ?

---
Concepts - advanced
Concepts - advanced
gcc has a new mechanism for concept checking.
To activate it define:_GLIBCXX_CONCEPT_CHECKS
Warning: not clear if it helps or not.
Boost library has a Concept Check Library:
http://www.boost.org/libs/concept_check/concept_check.htm
template<typename T> const T& min(const T& x,
const T& y)
{
   BOOST_CONCEPT_ASSERT((LessThanComparable <T>));
   return x < y? x : y;
}

---
Concepts
Concepts
A concept is a list of requirements on a type.
STL defines a hierarchy of concepts for containers,
iterators, and element types.
Concepts for element types include:
Equality Comparable -
types with operator== ,...
LessThan Comparable -
types with operator< ,...
Assignable -
types with operator=
and copy Ctor

---
Concepts
Concepts
Cleanly separate interface from implementation.
Primitives can also conform to a concept.

---
Concepts refinement
Concepts refinement
 Concept B is a refinement of concept A
 Concept B imposes some additional requirements on A
Similar to inheritance.

---
Main Components
Main Components
Algorithms
Containers
Iterators
Function
Objects
Adaptors
Streams
Strings

---
- Holds copies of elements.
- Assumes elements have:
  Copy Ctor & operator =
- The standard defines the interface.
- Two main classes
  - Sequential containers:
    list, vector,....
  - Associative containers:
    map, set ...
Assignable -
types with operator=
and copy Ctor
Containers

---
see http://www.cplusplus.com/reference/stl/
Containers documentation

---
Sequential Containers
Sequential Containers

---
Sequential Containers
Sequential Containers
Maintain a linear sequence of objects.
forward_list - a singly-linked list.
list - a doubly-linked list.
  1. Efficient insertion/deletion in front/end/middle
vector - an extendable sequence of objects
  1. Efficient insertion at end, and random access
deque – double-ended queue
  1. Efficient insertion/deletion at front/end
  2. Random access
array – fixed size, on the stack.

---
vector<T>
vector<T>
Contiguous array of elements of type T
Random access
Can grow on as needed basis
std::vector<int> v(2);
  v[0]= 45;
  v[1]= 32;
  v.emplace_back(60); //C++11

---
vector<T>
vector<T>
Contiguous array of elements of type T
Random access
Can grow on as needed basis
std::vector<int> v(2);
  v[0]= 45;
  v[1]= 32;
  v.push_back(60);// old style,
 // we will talk about
  // the difference

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
If we inserted n elements we paid:
1+2+1+4+1+1+1+8+…+n =
O(n) + 1+2+4+…+n =
O(n)
On average an each insertion cost O(1)

---
size and capacity
size and capacity
size
capacity
The first “size” elements are constructed (initialized)
The last “capacity - size” elements are uninitialized

---
size and capacity
size and capacity
- size_type size() const
- size_type capacity() const
size
capacity

---
C++ vs. Java
- Look at cplusplus documentation of vector.
- Look at Java documentation of Vector.
- Differences:
  - Simple class vs. interface and vtable.
  - Simple elements vs. class element.
  - Two accessors (with and without range check) vs. a single accessor

---
Creating vectors
Creating vectors
Empty vector:
std::vector<int> vec;
vector with 10 ints each one of value int()==0:
std::vector<int>	vec(10);
std::vector<int>	vec(10,0); // better
vector with 10 ints with the value of 42:
std::vector<int>	vec(10, 42);

---
Creating vectors
Creating vectors
Empty vector:
std::vector<int> vec;
vector with 10 ints each one of value int()==0:
std::vector<int>	vec(10);
std::vector<int>	vec(10,0); // better
Notice: int() is NOT a default constructor of int. Uninitialized ints (int k;) contain junk.

---
Creating vectors
Creating vectors
Empty vector:
std::vector<Fred> vec;
vector with 10 default constructed Fred objects. i.e: 10 Fred() objects:
std::vector<Fred> vec(10);
vector with 10 non-default constructed Fred objects:
std::vector<Fred> vec(10, Fred(5,7));

---
Creating vectors: C++11
Creating vectors: C++11
vector with different ints inside it:
std::vector<int> vec{1, 5, 10, -2, 0, 3};
vector with different Fred objects:
std::vector<Fred> vec{Fred(5,7), Fred(2,1) }
Or
std::vector<Fred> vec{ {5,7}, {2,1} }

---
Associated types in vector
Associated types in vector
vector<typename T>::
  1. value_type - The type of object, T, stored
  2. reference - Reference to T
  3. const_reference - const Reference to T
  4. iterator - Iterator used to iterate through a vector (how would you write it?)
  5. …

---
Time complexity
Time complexity
- Random access to elements.
- Amortized constant time insertion and removal of elements at the end.
- Linear time insertion and removal of elements at the beginning or in the middle.
- vector is the simplest of the STL container classes, and in many cases the most efficient.

---
Adding elements
Adding elements
Inserts a new element at the end:
void push_back(const T&)
    - a.push_back(t)
}
amortized constant time

---
Adding elements-C++11
Adding elements-C++11
Construct and insert a new element at the end:
    template<typename… Args>
void emplace_back(Args&&… args)
    1. a.emplace_back(t)
}
amortized constant time

---
Accessing elements
Accessing elements
Without boundary checking:
- reference operator[](size_type n)
- const_reference operator[](size_type n) const
With boundary checking:
- reference at(size_type n)
- const_reference at(size_type n) const

---
What about checking boundaries only in DEBUG mode? - Linux
What about checking boundaries only in DEBUG mode? - Linux
g++ has a standard library in DEBUG mode, to activate it define _GLIBCXX_DEBUG
   (g++ -D_GLIBCXX_DEBUG …)
stlport is an implementation of the standard library which includes DEBUG mode (havn't checked it myself yet):
http://www.stlport.org/

---
What about checking boundaries only in DEBUG mode? - MS
What about checking boundaries only in DEBUG mode? - MS
In MSVS 2012 Debug build is automatically safe and Release build mode is not
Other versions also have these kind of “Safe STL” modes but might require defining some flags to turn off or on.

---
vector<T>
vector<T>
Contiguous array of elements of type T
We can get the underlining T* pointer:
if size()>0
T* p= &(v[0])
c++11:
    T* p= v.data()

---
vector<T>
vector<T>
Contiguous array of elements of type T
We can get the underlining T* pointer:
if size()>0
T* p= &(v[0])
c++11:
T* p= v.data()
Useful for interfacing with C
or wrappers that work with C
like Matlab’s mex

---
vector<T> v
vector<T> v
v.shrink_to_fit() // c++11

---
Associative Containers
Associative Containers
Supports efficient retrieval of elements
(values) based on keys.
(Typical) Implementation:
red-black binary trees
hash-table (added in c++11)

---
Sorted Associative Containers
Sorted Associative Containers
set
A set of unique keys ordered by <
map
- Associate a value to key (associative array)
- Unique value of each key, ordered by <
multiset, multimap
Same, but allow multiple values
unordered_set, unordered_map
Same, but without order (faster).

---
Sorted Associative Containers & Order
Sorted Associative Containers & Order
Sorted Associative containers use operator<
as default order
We can control order by using our own
comparison function
To understand this issue, we need to use
function object
Function
Objects

---
Anything that can be called as if a function.
For example:
- Pointer to function
- A class that implements operator()
- Lambda expressions (c++11)
Function
Objects

---
Example
Example (folder 2)
class c_str_less {
public:
bool operator()(const char* s1,
        const char* s2) {
return (strcmp(s1,s2) < 0);
}
};
c_str_less cmp; // declare an object
if(cmp(“aa”,”ab”))
 …
if( c_str_less()(“a”,”b”) )
Creates temporary objects, and
then call operator()

---
Template comparator example
Template comparator example
template<typename T>
class less {
public:
bool operator()(const T& lhs, const T& rhs)
{ return lhs < rhs; }
};
less<int> cmp; // declare an object
if( cmp(1,2) )
 …
if( less<int>()(1,2) )
 …
Creates temporary objects,
and then call operator()

---
Using Comparators
Using Comparators
// ascending order
// uses operator < for comparison
set<int> s1;
set<int,less<int>> s1; // same
// descending order
// uses operator > for comparison
set<int,greater<int>> s2;

---
Using Comparators
Using Comparators
Creates a default constructed
MyComp object.
set<int,MyComp> s3;
MyComp cmp(42);
set<int,MyComp> s4(cmp);
Use given MyComp object.

---
Why should we use classes
as function objects?
Why should we use classes
as function objects?
- So we get the “power” of classes.
- Examples:
  - Inheritance.
  - To parameterize our functions in run time or in compile time.
  - To accumulate information.

---
Function object example:
dice code example
Function object example:
dice code example