C++: copy, assign, convert
Version 1: Dr. Ofir Pele
Version 2: Dr. Erel Segal-Halevi

---
Shallow vs. Deep Copy (folder 1)
class IntList {
   int* p;
public:
   IntList(uint n):
      p(new int[n]) { }
   ~IntList() {
      delete[] p; }
};
int main() {
   IntList a(3);
   IntList b=a;
   IntList c(2);
}
Stack
Heap	`
a.p
b.p / c.p
c.p[0]
c.p[1]
a.p[0]
a.p[1]
a.p[2]

---
Shallow vs. Deep Copy
class IntList {
   int* p;
public:
   IntList(uint n):
      p(new int[n]) { }
   ~IntList() {
      delete[] p; }
};
int main() {
   IntList a(3);
   IntList b=a;
   IntList c(2); c=a;
}
Stack
Heap	`
a.p
b.p / c.p
c.p[0]
c.p[1]
a.p[0]
a.p[1]
a.p[2]

---
Copying
An object is copied when:
Constructing new object from existing;
Passing parameter by value;
Returning by value;
Assigning existing to existing.
Cases 1-3 are handled by
        copy constructor;
Case 4 is handled by
        assignment operator.
By default, both do shallow copy.

---
What is it good for - 2
Rule of Three
A rule of thumb:
  - When you need to make a deep copy of an object, you need to define all of these:
    - Copy constructor
    - Destructor
    - Operator =
  - Or in other words:
when you need one, you need all.

---
A skeleton for deep copy
A skeleton for deep copy (folder 1)
// Copy constructor
A (const A& other) : init {
copy_other(other);
}
// Operator =
A& operator=(const A& other) {
if (this!=&other) { // preventing problems in a=a
  clear(); init // or recycle
  copy_other(other);
} return *this; } // allows a= b= c= …
// Destructor
~A() {
clear();
}

---
Conversions of types is done in two cases:
Conversions of types
done in two cases:
  1. Explicit casting;
  2. When a function gets X type while it was expecting to get Y type, and there is a casting from X to Y:
void foo(Y y)
...
X x;
foo(x); // a conversion from X to Y is done

---
User defined conversion
User defined conversion (folders 5,6)
class Fraction {
...
// double --> Fraction conversion
Fraction (const double& d) {
...
}
...
// Fraction --> double conversion
operator double() const {
...
}
...

---
Conversions danger:
	unexpected behavior
Conversions danger:
unexpected behavior
Vector(size_t length) // ctor
…
int sum(const Vector& v) // function
...
int i=3;
sum(i); // Equivalent to: sum(Vector(i))
// Did the user really wanted this?
The Vector and the size_t objects are not logically the same objects!

---
The explicit keyword (folder 4)
explicit Vector(size_t length) // ctor
…
int sum(const Vector& v) // function
...
int i=3;
sum(i); // Won’t compile